## Slide 1
Radio Software
Huawei Active Antennas
Design Guideline
September 2014
C2

## Slide 2: Types of AA - Definition
VELCRO
RU attached to the back side of the antenna
SMART
Array of active elements interconnected to the antenna
C2

## Slide 3: Types of AA – Available Models for Rollout
VELCRO
RU attached to the back side of the antenna
High Bands active
SMART
Integrated RU with beamforming capabilities
High Bands active
AAU3911
C2

## Slide 4: AAU3902 – Smart AA Solution
C2
AAU3902 is a 2.0 m triple-array antenna solution capable to provide active TX beamforming
  Active beamforming is available for higher bands, AAU3902 can handle up to 2 active bands/RAT at a time
  Up to 5 bands can be radiated using a single AAU3902 antenna (external combiners may be needed, depending on bands combination)
AAU3902 is suitable for site configurations with 1 antenna per sector.
  In case of 2 antennas/sector, AAU3902 shall be dedicated to ‘active’ higher bands features leaving ‘passive’ bands to ‘legacy’ antenna
AAU3902 provides a couple of remarkable beamforming features (available for 3G and 4G)
  Vertical 4way RX (UL only): increases UL traffic and reduces the UL load
  Vertical Multiple Sectors (UL & DL): increases UL/DL cell capacity
  Such features can be switched on alternatively and cannot coexist
  Other features are available, as well
AAU3902 is available from SRAN8.0 onwards

## Slide 5: AAU3911 – Velcro AA Solution
C2
AAU3911 is the Velcro solution from Huawei portfolio
  RRU integrated in the antenna
  No TX active beamforming available
AAU3911 is a 2.0 m triple-array antenna capable to provide 4 way UL diversity (2T4R)
  A low-band passive array handles 800 and 900MHz bands (with ext. combiners)
  A couple of high band arrays handle up to 2 active bands (1.8A, 2.1A or 2.6A)
  Also ready for 1.8P+2.1P (2T2R) (needs integrated combiner)
  Antenna-integrated RRUs can provide up to 2x60W RF power
AAU3911 ensures horizontal 4 way UL diversity using a couple of high-band arrays
  Horizontal 4way diversity: the 2 Xpol arrays have the same coverage footprint
AAU3911 is available from 4Q2014

## Slide 6: AAU3911 – Velcro AA Solution
C2
AAU3911C 2.1A

## Slide 7: Passive vs. Active Antenna – General Specifications
 | Passive | Velcro | Smart
PIM | Low quality installation | NO | NO
Cable losses (w/ RRU) | 0,48dB – 5,97dB (typ. 1,5dB) | NO | NO
4-way diversity | With 4 ports (only 2.6GHz) | YES (high bands) | YES (high bands)
RET | Ready old models Integrated new models | Integrated | Integrated
Roadmap | Very extensive | Limited | Limited
Poles for full bands | 1 | 1 or 2 | 1 or 2
Passive Sharing | YES | Limited | Limited
Power | 2x40W or 2x60W | 2x40W or 2x60W | 2x40W
Modular RU | YES | YES | YES
MDT | YES | tbd | 3º
C2

## Slide 8: Active Antenna – Specifications
C2

## Slide 9: Active Antenna – Roadmap
C2

## Slide 10: Smart Antenna Features
C2
Feature activation per carrier

## Slide 11: AAU3902 – Beamforming Features Compatibility
C2
 | V4R | vertical sectorization | independent tilt per carrier | independent tilt UL/DL | V4T
V4R | - | NO | YES Beam 1 - Beam 2 = VHPBW | YES Beam 1 - Beam 2 = VHPBW | YES Beam 1 - Beam 2 = VHPBW Same tilt for V4T and V4R
independent tilt UL/DL | - | YES Beam 1 - Beam 2 < VHPBW | - | - | YES Beam 1 - Beam 2 = VHPBW
independent tilt per carrier | - | YES Tilt beam1 - beam2 of F1 = VHPBW Tilt Beam1 - Beam2 of F2 < VHPBW | - | - | YES Tilt beam1 - beam2 of F1 = VHPBW Tilt Beam1 - Beam2 of F2 < VHPBW

## Slide 12: Site Evolution with AAU (example)
C2

## Slide 13: Site Evolution: Target configuration with AAU (example)
C2

## Slide 14: Application Scenarios: General Rules
C2
AA is the first option to take into account if it is needed to act over a site, and antenna replacement is necessary or new RRU outdoor placement it is not feasible. Main scenarios are: New site, LTE upgrade, RAN Refresh or 3G capacity upgrade.
When a new AA is deployed we must assure future proof, in order to allow most probable bands deployment (800, 900, 1800, 2100 and 2600MHz).
Regarding passive site sharing, when a new AA is deployed we must assure that current or potential future sharing in the site is feasible without AA remove, at least for one additional operator.
Where RRU indoor equipment is removed, AA provide remarkable energy savings.

## Slide 15: AAU3902 – Advantages and Drawbacks
C2
Main advantages:
  Triple-array broad band antenna, handling 5 bands (with ext. combiner)
  Up to 2 active bands on separate arrays (1.8A+2.1A)
  Independent tilt per band
  Low RF losses, similar EIRP of 2x60W RRU
  Different ‘active‘ features available depending on scenario/traffic needs
  Capable to handle high capacity traffic in a number of network scenarios
  Energy savings (reduced power consumption)
  Performance improvement seen on field
Drawbacks:
  Heavy weight (>50 Kg) may be a limiting factor for installations
  Not suitable for replacement of 1.3 m or slim passive antennas
  Increased hardware complexity
  Some beamforming features cannot coexist
  GL1800 configurations requires SingleOM and GBBP/UBBP boards

## Slide 16: AAU3911 – Advantages and Drawbacks
C2
Main advantages:
  Triple-array broad band antenna, handling 5 bands (with ext. combiner)
  Up to 2 active bands for 2T4R
  Low RF losses, same or better EIRP of 2x60W RRU
  Energy savings (reduced power consumption), mainly for indoor RRU
Drawbacks:
  Heavy weight (near 50 Kg) may be a limiting factor for installations
  Not suitable for replacement of 1.3 m or slim passive antennas
  To handle 5 bands in a single antenna could limit 2R4T capabilities
  Limited independent tilt per band

## Slide 17: AAU39xx – Use Case: 3G Capacity
17
Sites with 4 carriers deployed, and capacity upgrade necessary
  AAU3902 2.1A (V4R or VMS)
Constraints for AA use:
  Site shared or potentially shared: One antenna for only VDF use (as an exception, feasible to use AAU3902 passive ports to share)
  No slim site
  With LTE2600, necessary 2 antenna to maintain 2T4R
  Infra requirements
  65º horizontal beamwidth
  2x40W AAU3902 2.1A, potential slight coverage decrease (depending baseline RRU placement)

## Slide 18: AAU39xx – Use Case: 3G Capacity
Fulfill AAU3902 constraints?
N
LTE1800
Cosite?
Y
3G site 4 carriers/sector and new carrier needed
18
FY2014-15
Q3
FY2014-15
Q4
FY2015-16
(Single OM)
N
AAU3902 2.1A
V4R or VMS (*)
Horizontal
Sectorisation
Y
AAU3902 2.1A
V4R or VMS
(*) (**)
AAU3902 1.8A+2.1A
V4R or VMS (*) (****)
DCS
Cosite?
N
Y
AAU3902 2.1A
V4R or VMS (*) (***)
AAU3902 1.8A+2.1A
V4R or VMS (*) (****)
(**) SRAN9.0 for 2 Active bands
(***) Single OM for GL mode
(*) RRU2100 reuse in other site
(****) RRU1800 reuse in other site

## Slide 19: AAU39xx – Use Case: New Site
19
New site deployed
  AAU3911 2.1A (H4R), and 1.8A (H4R) if LTE1800 needed since 1Q2015.
  AAU3902 2.1A and 1.8A for hot spot sites
Constraints for AA use:
  Site shared or potentially shared: One antenna for only VDF use (as an exception, feasible to use AAU3902 passive ports to share)
  No slim site
  Infra requirements
  65º horizontal beamwidth
  2 active bands since 1Q2015 and SRAN9.0

## Slide 20: AAU39xx – Use Case: New Site
Fulfill AAU39xx constraints?
N
Hot Spot
>3 3G carriers?
Y
New site
20
FY2014-15
Q3
FY2014-15
Q4
FY2015-16
(Single OM)
N
Passive
Solution
Y
LTE1800
needed?
N
U2100 or LTE1800 needed?
N
AAU3911 2.1A
H4R
Y
AAU3902 2.1A
V4R or VMS
AAU3902 1.8A
V4R or VMS (**)
AAU3902 1.8A+2.1A
V4R or VMS
DCS
needed?
N
Y
AAU3902 2.1A
V4R or VMS (***)
AAU3902 1.8A+2.1A
V4R or VMS
(**) SRAN9.0 for 2 Active bands
Y
AAU3902 2.1A
V4R or VMS
LTE1800
needed?
N
AAU3902 1.8A
V4R or VMS
AAU3911 1.8A+2.1A
H4R
DCS
needed?
Y
N
AAU3902 2.1A
V4R or VMS (***)
AAU3911 1.8A+2.1A
H4R
Y
(***) Single OM for GL mode

## Slide 21: AAU39xx – Use Case: LTE Upgrade/RAN Refresh
21
LTE Upgrade with antenna change or new RRU without installation place
  4 carrier sites: AAU3902 1.8A (V4R or VMS) (2.1A if G1800 cosite)
  <4 carrier sites: AAU3911 2.1A (H4R) (1.8A since 2Q2015)
Constraints for AA use:
  Site shared or potentially shared: One antenna for only VDF use. As an exception, feasible to use AAU3902 passive ports to share
  No slim site
  With LTE2600, necessary 2 antenna to maintain 2T4R
  Infra requirements
  65º horizontal beamwidth
  2x40W AAU3902 2.1A, potential slight coverage decrease
  2 active bands Huawei AAU since 1Q2015 and SRAN9.0

## Slide 22: AAU39xx – Use Case: LTE1800 Upgrade
Fulfill AAU39xx constraints?
N
Hot Spot
>3 3G carriers?
Y
LTE1800 upgrade with antenna change or new RRU without outdoor place
22
FY2014-15
Q3
FY2014-15
Q4
FY2015-16
(Single OM)
N
AAU3902 1.8A
V4R or VMS
Passive
Solution
Y
AAU3911 1.8A
H4R
AAU3902 1.8A
V4R or VMS (**)
AAU3902 1.8A+2.1A
V4R or VMS (*)
DCS
Cosite?
N
Y
AAU3902 2.1A
V4R or VMS (*) (***)
AAU3902 1.8A+2.1A
V4R or VMS (*)
(**) SRAN9.0 for 2 Active bands
(***) Single OM for GL mode
DCS
Cosite?
N
Y
Passive
Solution (***)
AAU3911 1.8A
H4R
(*) RRU2100 reuse in other site
N

## Slide 23: AAU39xx – Use Case: LTE800 Upgrade
Fulfill AAU39xx constraints?
N
Hot Spot
>3 3G carriers?
Y
LTE800 upgrade with antenna change or new RRU without outdoor place
23
FY2014-15
Q3
FY2014-15
Q4
FY2015-16
N
Passive
Solution
Y
AAU3902 1.8A
V4R or VMS
(**) (****)
AAU3902 1.8A+2.1A
V4R or VMS (*) (****)
DCS
Cosite?
N
Y
AAU3902 2.1A
V4R or VMS (*) (***)
AAU3902 1.8A+2.1A
V4R or VMS (*) (****)
(**) SRAN9.0 for 2 Active bands
(***) Single OM for GL mode
U2100 or LTE1800 Cosite?
N
Y
AAU3902 2.1A
V4R or VMS (*)
AAU3911 2.1A
H4R (*)
N
LTE1800
Cosite?
N
Y
Passive
Solution
AAU3911 1.8A
H4R (****)
(*) RRU2100 reuse in other site
DCS
Cosite?
N
Passive
Solution (***)
AAU3911 1.8A
H4R (****)
Y
(****) RRU1800 reuse in other site
RRU place
N
Y

## Slide 24: AAU39xx – Use Case: RAN Refresh/3G Only Upgrade
Fulfill AAU39xx constraints?
N
Hot Spot
3 U2100 carriers?
Y
RR o 3G upgrade with antenna change or new RRU without outdoor place
24
FY2014-15
Q3
FY2014-15
Q4
FY2015-16
N
Passive
Solution
Y
AAU3902 1.8A
V4R or VMS
(**) (****)
AAU3902 1.8A+2.1A
V4R or VMS (*) (****)
DCS
Cosite?
N
Y
AAU3902 2.1A
V4R or VMS (*) (***)
AAU3902 1.8A+2.1A
V4R or VMS (*) (****)
(**) SRAN9.0 for 2 Active bands
(***) Single OM for GL mode
U2100 or LTE1800 Cosite?
N
Y
AAU3902 2.1A
V4R or VMS (*)
AAU3911 2.1A
H4R (*)
N
LTE1800
Cosite?
N
Y
Passive
Solution
AAU3911 1.8A
H4R (****)
(*) RRU2100 reuse in other site
DCS
Cosite?
N
Passive
Solution (***)
AAU3911 1.8A
H4R (****)
Y
(****) RRU1800 reuse in other site
RRU place
N
Y

## Slide 25: Backup

## Slide 26: AAU3902 – Vertical 4 UL Channels 1/2
It implements 4-way antenna receive diversity. It just affects UL traffic.
4 way RX diversity provides better signal quality on the uplink so the advantage of such feature is dual:
  It helps to keep the UL load under control (same UL throughput achieved with lesser UL load)
  It increases the UL throughput in poor coverage areas.
Results confirmed by trial
V4RX

## Slide 27: AAU3902 – Vertical 4 UL Channels 2/2
V4R is achieved through the overlapping of a second X polarised beam (dubbed ‘inner beam’ – used for UL only) whose footprint is different (and smaller) than the original beam (‘outer beam’) providing primary DL/UL coverage.
Dual UL coverage is truly effective in the portion of the original cell where inner and outer beams are superimposed.
UL load is reduced on the whole original cell, therefore any user of the original cell takes advantage of the additional receivers even if the 2 beams are not totally overlapped.
Outer beam (UL+DL)
Inner beam (UL)
Dual UL Coverage

## Slide 28: AAU3902 – Vertical Multiple Sectors
VMS
It splits a sector into an inner cell and an outer cell. It affects both UL/DL traffic.
  Overall RRU power is divided for inner and outer cells (also not symmetrically)
Cell overlap depends on beams tilt:
  Cell splitting increases the single user throughput as more resources are available,
  Overall interference (particularly at cell edges) may be reduced,
  An excessive cells overlap may raise the interference in the inner cells.
Such a feature, to be truly effective, may require a general re-alignment of the antenna parameters (antennas downtilt angles) of surrounding sites.
  It may be an issue if RET for passive antenna is not available for installed antennas

## Slide 29: AAU3902 – Indipendent Tilt for UL and DL
In ‘traditional’ coverage with RxUs and legacy antennas UL and DL downtilt angles are the same
In cells served by AAU3902, the Independent Tilt for Uplink and Downlink feature enables different downtilt angles for uplink and downlink beams
It is possible to balance uplink and downlink coverage.
The benefit of Independent tilt UL/DL strongly depends on the network scenario, it may be considered as an additional optimization tool for cells fine tuning.
VMS

## Slide 30: Horizontal vs Vertical Sectorization
Horizontal Sectorization (Conventional)
Achieved swapping existing 65° passive antennas with dual beam ones
  Each beam is narrower and covers a portion of the original cell
  The footprint of the resulting cells is typically bigger than the original one
  Application is limited by narrow-beam antennas availability
New RF modules are added
  Overall power increased (may be doubled)
  Interference issues
Vertical Sectorization (AAU3902)
Feature Activation triggered by traffic needs
  Inner and outbeam can be optimized (Tilt, Power)
  Feature can be switched off if needed (and other features activated)
  Interference mitigation is easier than with conventional horizontal sectorization with passive antennas
Overall AAU RF power is split among inner/outer cells
  The overall power (EiRP) is not increased.
  Reduced interference (and it can be mitigated by changing inner/outer downtilts)

## Slide 31: Smart Features – Main Results V4R
UMTS
LTE

## Slide 32: Smart Features – Main Results VMS
UMTS Coverage
Passive
UMTS Coverage
Active VMS
C2

## Slide 33: Smart Features – Main Results VMS
UMTS EcIo
Passive
UMTS EcIo
Active VMS
C2

## Slide 34: Smart Features – Main Results VMS
C2
LTE UL

## Slide 35: Smart Features – Main Results VMS
C2
LTE DL