| HOP ID 3858 A SITE ID _Name: ZU083 Alpha Bank B SITE ID _Name: BU379 Stavrinos Check 1. GENERAL 2. HOP CONFIGURATION 3. START OF INSTALLATION 4. INSTALLATION IU-OU 5. INTEGRATION 6. ATTACHMENTS |  |
| --- | --- |

- GENERAL

| Site folder implemented by: | Mihailescu Iulian |
| --- | --- |
| Site folder checked by (Egnatia Rom): |  |
| Date of installation end: | 02.11.2009 |
| Date of Integration end: | 04.11.2009 |
| Hop ID: | 3858 |
| Site A name: | Alpha-Bank | Site B name: | Stavrinos |
| Site A ID: | ZU083 | Site B ID: | BU379 |
| Site A ID-Hop: | 3858 | Site B ID-Hop: | 3858 |
| Site A Address-region: | BUC | Site B Address-region: | BUC |
| Site A special info(keys, owner): | Special, Cosmote |
| Site B special info(keys, owner): | Special, Cosmote |

2. HOP CONFIGURATION

| Hop Length: | 1,83Km |
| --- | --- |
| Capacity |  | Operation mode: |  |
| Polarization |  | Frequency Band: | 38 GHz |
| SITE A | SITE B |
| TX Frequency (A) | 39168.5 | TX Frequency (B): | 37908.5 |
| TX Power (A) | 8 | TX Power (B) | 8 |
| TX Attenuator (dB) (A) | n/a | TX Attenuator (dB) (B) | n/a |
| MW Antenna main size (A) | 0.6 m | MW Antenna main size (B): | 0.6 m |
| MW Antenna div size (A) | n/a | MW Anten div size (B): | n/a |
| High of main Antenna (A) | 37 | High of Main Antenna (B) | 42 |
| High of Div Antenna (A) | n/a | High of Div Antenna (B) | n/a |
| Length of pole Main Ant(A) | 1 m | Length of pole main Ant(B) | 3 m |
| Length of pole Div Ant(A) | n/a | Length of pole Div Ant(B) | n/a |
| Direction of MW Ant(s) (A) | 91 | Direction of MW Ant(s) (B) | 271 |
| SW Version of IU(s) (site A) | n/a | SW Version of IU(s) (site B): | n/a |
| SW Version of OU(s) (A) |  | SW Version of OU(s) (B) |  |
| Version(PN) of OU(s) (site A) |  | Version(PN) of OU(s) (site B): |  |
| Serial Numbers of IU(s) (A) |  | Serial Numbers of IU(s) (B) |  |
| Serial Numbers of OU(s) (A) |  | Serial Numbers of OU(s) (B) |  |
| Serial Numbers of Ant(s) (A) |  | Serial Numbers of Ant(s) (B) |  |
| IP Address (A) |  | IP Address (B) |  |

3.  START OF INSTALLATION

|  | OK | N.OK | N/A |
| --- | --- | --- | --- |
| Completeness of materials on site |  |  |  |
| Delivery checked, shortcomings recorded |  |  |  |
| Equipment layout checked, differences to the drawings recorded |  |  |  |
| Installation of shelter-room-Outdoor equipment readiness |  |  |  |
| Installation of tower-mast- MW poles readiness |  |  |  |
| IF routes checked, cable trays installed |  |  |  |
| Site Acceptable in order to start the installation according specifications |  |  |  |

| Remarks: |  |
| --- | --- |

4.  INSTALLATION IU-OU

| 4.1 RADIO LINK CABINET-IU INSTALLATION SITE A | OK | N.OK | N/A |
| --- | --- | --- | --- |
| Cabinets fixed to wall or floor, secured and feet adjusted |  |  |  |
| Check for the typical clearances according the specifications |  |  |  |
| Each cabinet connected to main grounding bus bar |  |  |  |
| Installation of power distribution board (PDU) on cabinet (higher part) |  |  |  |
| Power cables connected on power cabinet and labelled correctly |  |  |  |
| Power cables connected on correct positions and labelled (on PDU) |  |  |  |
| Installation of Indoor unit (IU) according the specifications (lower part) |  |  |  |
| Grounding of IU (if needed) |  |  |  |
| Power cables connected on IU and labelled correctly (on PDU) |  |  |  |
| 2 Mbits frames are installed and labelled (on 2Mbits frame) |  |  |  |
| All necessary 2 Mbits cables are installed and arranged in cabinet |  |  |  |
| All 2Mbit channels looped |  |  |  |
| IF cable is connected on input of IU |  |  |  |
| All the cables are labelled, formed and tied |  |  |  |
| Check the DC supply for IU(s) |  |  |  |
| Check the power on of the IU |  |  |  |

| Remarks: |  |
| --- | --- |

| 4.2 RADIO LINK CABINET-IU INSTALLATION SITE B | OK | N.OK | N/A |
| --- | --- | --- | --- |
| Cabinets fixed to wall or floor, secured and feet adjusted |  |  |  |
| Check for the typical clearances according the specifications |  |  |  |
| Each cabinet connected to main grounding bus bar |  |  |  |
| Installation of power distribution board (PDU) on cabinet (higher part) |  |  |  |
| Power cables connected on power cabinet and labelled correctly |  |  |  |
| Power cables connected on correct positions and labelled (on PDU) |  |  |  |
| Installation of Indoor unit (IU) according the specifications (lower part) |  |  |  |
| Grounding of IU (if needed) |  |  |  |
| Power cables connected on IU and labelled correctly (on PDU) |  |  |  |
| 2 Mbits frames are installed and labelled (on 2Mbits frame) |  |  |  |
| All necessary 2 Mbits cables are installed and arranged in cabinet |  |  |  |
| All 2Mbit channels looped |  |  |  |
| IF cable is connected on input of IU |  |  |  |
| All the cables are labelled, formed and tied |  |  |  |
| Check the DC supply for IU(s) |  |  |  |
| Check the power on of the IU |  |  |  |

| Remarks: |  |
| --- | --- |

| 4.3 RADIO LINK ANTENNA-OU INSTALLATION SITE A | OK | N.OK | N/A |
| --- | --- | --- | --- |
| MW Antennas are assembled according specifications |  |  |  |
| Alignment units are assembled according specifications |  |  |  |
| MW Antennas and Alignment units set up properly |  |  |  |
| Installation of poles are according to the work order (w.o) |  |  |  |
| All necessary safety precautions taken for the installation |  |  |  |
| MW antennas are installed according specifications and w.o |  |  |  |
| Side supports installed according specifications (ω<25ο) |  |  |  |
| Outdoor Units are installed according specifications |  |  |  |
| Grounding of Outdoor Units |  |  |  |
| Connectors at OUs are implemented and tightened (mechanical check) |  |  |  |
| 1m over plus of IF cables near to OUs |  |  |  |
| OUs connectors weatherproofed |  |  |  |
| IF cables route on cable ladders with clamps (no sharp bending) |  |  |  |
| Ground of IF cable near to ODU and outside of room-RBS |  |  |  |
| Cable entry is waterproofed |  |  |  |
| Labels are mounted to the IF cables (hop numbers at top and bottom) |  |  |  |

| Remarks: |  |
| --- | --- |

| 4.4 RADIO LINK ANTENNA-OU INSTALLATION SITE B | OK | N.OK | N/A |
| --- | --- | --- | --- |
| MW Antennas are assembled according specifications |  |  |  |
| Alignment units are assembled according specifications |  |  |  |
| MW Antennas and Alignment units set up properly |  |  |  |
| Installation of poles are according to the work order (w.o) |  |  |  |
| All necessary safety precautions taken for the installation |  |  |  |
| MW antennas are installed according specifications and w.o |  |  |  |
| Side supports installed according specifications (ω<25ο) |  |  |  |
| Outdoor Units are installed according specifications |  |  |  |
| Grounding of Outdoor Units |  |  |  |
| Connectors at OUs are implemented and tightened (mechanical check) |  |  |  |
| 1m over plus of IF cables near to OUs |  |  |  |
| OUs connectors weatherproofed |  |  |  |
| IF cables route on cable ladders with clamps (no sharp bending) |  |  |  |
| Ground of IF cable near to ODU and outside of room-RBS |  |  |  |
| Cable entry is waterproofed |  |  |  |
| Labels are mounted to the IF cables (hop numbers at top and bottom) |  |  |  |

| Remarks: |  |
| --- | --- |

5.  INTEGRATION

| 5.1 ALIGNMENT OF HOP | OK | N.OK | N/A |
| --- | --- | --- | --- |
| Frequencies set according the work order (w.o) |  |  |  |
| TX power according the work order (w.o) |  |  |  |
| Set TX power on |  |  |  |
| Alignment of Hop according the directions of w.o |  |  |  |
| Alignment Completed correctly |  |  |  |
| All needed bolt nuts are tighten properly |  |  |  |

| 5.2 INTEGRATION OF HOP |
| --- |
| Receive level from w.o (A) | -32.87 | Receive level from w.o (B) | -32.87 |
| Receive level from commissioning (A) | -31.9 | Receive level from commissioning (B) | -32.5 |
| Interference test (A) | dBm | Interference test (B) | dBm |
| Active Alarms on site A |  | Active Alarms on site B |  |
| Traffic cable and connection test (A) |  | Traffic cable and connection test (B) |  |
| Performance test site A |  | Performance test site B |  |
| Site A clean of rubbishes |  | Site B clean of rubbishes |  |
| Loop Test of LIU(B) and BER measurement (A) | -dBm | Loop Test of LIU(A) and BER measurement (B) | -dBm |

| S I T E (A) | S I T E (B) |
| --- | --- |
| CHANNEL | Destination | CHANNEL | Destination | CHANNEL | Destination | CHANNEL | Destination |
| CH1 | Alpha-Bank | CH2 | available | CH1 | available | CH2 | available |
| CH3 | available | CH4 | available | CH3 | available | CH4 | available |
| CH5 |  | CH6 |  | CH5 |  | CH6 |  |
| CH7 |  | CH8 |  | CH7 |  | CH8 |  |
| CH9 |  | CH10 |  | CH9 |  | CH10 |  |
| CH11 |  | CH12 |  | CH11 |  | CH12 |  |
| CH13 |  | CH14 |  | CH13 |  | CH14 |  |
| CH15 |  | CH16 |  | CH15 |  | CH16 |  |

| Remarks: |  |
| --- | --- |

| 6.9 ATTACHMENTS | OK | N.OK | N/A |
| --- | --- | --- | --- |
| Work order inside the site folder |  |  |  |
| Material list inside the work order |  |  |  |
| Complete of remarks inside the site folder |  |  |  |
| Photos inside the site folder |  |  |  |
| INSTALLATION PHOTOS |
| General Site View |  |  |  |
| General tower View with MW Antenna |  |  |  |
| View of back of MW Antenna |  |  |  |
| View of RAU |  |  |  |
| Insulation of RG cable on RAU |  |  |  |
| View of flexible guide |  |  |  |
| Route of RG cable on tower-trays |  |  |  |
| Groundings of RG cable |  |  |  |
| Cable tray and cable entry of RG cable |  |  |  |
| AMM with MMU |  |  |  |
| Digital Distribution (Krone panel) frame |  |  |  |